## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 06

## Slide 2: ZENER REGION
If the Diode is reverse biased and the voltage is increased, a point will be reached when the diode enters reverse breakdown and current will flow with a very rapid rate.
The direction of this current will be opposite to that of the positive voltage region.
The reverse bias potential that results in this dramatic change in characteristics is called the Zener Potential /Voltage and is given by the symbol Vz.
The reverse or Avalanche breakdown is often termed as Zener Breakdown (at very low levels).

## Slide 3
A zener diode operates in reverse bias.
Common Zener Voltages: 1.8V to 200V.
ZENER DIODE

## Slide 4
The off state is defined by a voltage less than Vz but greater than 0V. The Zener equivalent is the open circuit.
ZENER DIODE

## Slide 5
The Zener diode is a heavily doped diode which, as a result of doping, has a very narrow depletion region. This allows the diode to be operated in the reverse biased region of the characteristic curve without damaging the PN junction.
Because of its higher temperature and current capability, silicon is usually preferred in manufacture of Zener Diodes.
Zener Diodes provide a stable reference voltage for use in power supplies, voltmeter & other instruments, voltage regulators.
ZENER DIODE

## Slide 6
ZENER DIODE EXAMPLE

## Slide 7
ZENER DIODE EXAMPLE

## Slide 8: 1st CONDITION: Vi AND R FIXED
The simplest of Zener diode regulator networks appears in Fig. 2.112 . The applied dc voltage is fixed, as is the load resistor. The analysis can fundamentally be broken down into two steps.
1. Determine the state of the Zener diode by removing it from the network and calculating the voltage across the resulting open circuit.
If V ≥ VZ, the Zener diode is on, and the appropriate equivalent model can be substituted.
If V < VZ, the diode is off, and the open-circuit equivalence is substituted.

## Slide 9: 1st CONDITION: Vi AND R FIXED
2. Substitute the appropriate equivalent circuit and solve for the desired unknowns.
For the network of Fig. 2.112 , the “on” state will result in the equivalent network of Fig.2.114 . Since voltages across parallel elements must be the same, we find that
The power dissipated by the Zener diode is determined by
That must be less than the PZM specified for the device.

## Slide 10: 1st CONDITION: Vi AND R FIXED

## Slide 11: 1st CONDITION: Vi AND R FIXED

## Slide 12: 1st CONDITION: Vi AND R FIXED

## Slide 13
Due to the offset voltage Vz, there is a specific range of resistor values (and therefore load current) which will ensure that the Zener diode is in the on state.
Too small RL  VL < Vz  Zener diode will be in the off state.
To determine the min RL that will turn the Zener diode on :
Any load resistance value greater than the RL min will ensure that the Zener diode is in the on state and the diode can be replaced by its Vz source equivalent.
The max IL
2nd CONDITION: FIXED Vi, VARIABLE RL

## Slide 14
Once the diode is in the on state, the voltage across R remains fixed at:
Iz is limited to IZM as provided on the data sheet, it does affect the range of RL and therefore IL.
The maximum load resistance
See Example 2.27.
2nd CONDITION: FIXED Vi, VARIABLE RL

## Slide 15
For fixed values of RL, the voltage Vi must be sufficiently large to turn the Zener diode on. The min turn-on voltage Vi=Vi min :
The max value of Vi is limited by the max Zener current IZM.
Since IL is fixed at VZ/RL and IZM is the max value of IZ, the max Vi is defined by:
3rd CONDITION: FIXED RL, VARIABLE Vi

## Slide 16
3rd CONDITION: FIXED RL, VARIABLE Vi

## Slide 17
Thank You