## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 08

## Slide 2
The proper biasing of the common-base configuration in the active region can be determined quickly using the approximation IC IE and assuming for the moment that IB 0 mA.
The result is the configuration of Fig. 3.11 for the pnp transistor.
For the npn transistor the polarities will be reversed.
BIASING

## Slide 3: COMMON-EMITTER CONFIGURATION
It is called common-emitter configuration since :
    emitter is common or reference to both input and output terminals.
    emitter is usually the terminal closest to or at ground potential.
Almost all amplifier design is using connection of CE due to the high gain for current and voltage.
Two set of characteristics are necessary to describe the behavior for CE:
    input (base terminal) and
    output (collector terminal) parameters.

## Slide 4: COMMON-EMITTER CONFIGURATION

## Slide 5: COMMON-EMITTER CONFIGURATION
IB is micro-amperes compared to milli-amperes of IC.
IB will flow when VBE > 0.7V for silicon and 0.3V for germanium
Before this value IB is very small.
Base-emitter junction is forward bias
Increasing VCE will reduce IB for different values.
Input characteristics for a
common-emitter n-p-n transistor

## Slide 6: COMMON-EMITTER CONFIGURATION
For small VCE (VCE < VCESAT, IC increase linearly with increasing of VCE
VCE > VCESAT, Independent of VCE  constant IC
IB(uA) is very small compare to IC (mA). Small increase in IB cause big increase in IC
Output characteristics for a
common-emitter n-p-n transistor

## Slide 7: COMMON-EMITTER CONFIGURATION
ACTIVE REGION | SATURATION REGION | CUTOFF REGION
BE junction is forward biased | BE and CB junctions are forward biased, thus the values of IB and IC is too big | Region below IB = 0 µA is to be avoided if an undistorted output signal is required
CB junction is reverse biased | The value of VCE is too small | BE junction and CB junctions are reverse biased
Can be employed for voltage, current and power amplification | Suitable region when the transistor is used a logic switch | IB = 0, IC not zero, during this condition IC = ICEO where this is the current flow when BE is reverse biased
 | NOT and avoid this region when the transistor as an amplifier | 

## Slide 8: BETA (β) OR AMPLIFICATION FACTOR
The ratio of dc collector current (IC) to the dc base current (IB) is dc beta (βdc ) which is dc current gain where IC and IB are determined at a particular operating point, Q-point (quiescent point).
It’s defined by the following equation:
On data sheet, βdc= hFE with h is derived from ac hybrid equivalent circuit. FE are derived from forward-current amplification and common-emitter configuration respectively.
For ac conditions an ac beta has been defined as the changes of collector current (IC) compared to the changes of base current (IB) where IC and IB are determined at operating point.
It can be defined by the following equation:

## Slide 9: RELATIONSHIP ANALYSIS BETWEEN α AND β

## Slide 10: COMMON–COLLECTOR CONFIGURATION
The output voltage is obtained at emitter terminal.
The input characteristic of common-collector configuration is similar with common-emitter configuration.
Common-collector circuit configuration is provided with the load resistor connected from emitter to ground.
It is used primarily for impedance-matching purpose since it has high input impedance and low output impedance.

## Slide 11: COMMON–COLLECTOR CONFIGURATION

## Slide 12: LIMITS OF OPERATION
Many BJT transistor used as an amplifier. Thus it is important to notice the limits of operations.
There are few rules that need to be followed for BJT transistor used as an amplifier. The rules are:
    transistors need to operate in active region!
    IC < Icmax
    PC < PCmax

## Slide 13
Thank You