## Slide 1: Thermodynamics Lecture 01
Basic Mechanical Engineering

## Slide 3: THERMODYNAMICES
THERMO--- Heat Released
DYNAMICS ----- Mechanical Action For doing work
The study of the effects of work, heat flow, and energy on a system
Movement of thermal energy
Engineers use thermodynamics in systems ranging from nuclear power plants to electrical components.
Thermodynamics is the study of the effects of work, heat, and energy on a system
Thermodynamics is only concerned with macroscopic (large- scale) changes and observations

## Slide 4
BOUNDARY- | System | & Surrounding | are
separated by | some | Imaginary Or | real
SYSTEM, SURROUNDING ,UNIVERSE
SYSTEM-Area under thermodynamic study
SURROUNDING – Area outside the system
Surface/Layer/Partition
UNIVERSE – System & together is called Universe
Surroundings put

## Slide 5: ISOLATED, CLOSED AND OPEN SYSTEMS
4
Isolated System
Neither energy nor mass can be exchanged.
E.g. Thermo flask
Closed System
Energy, but not mass can be exchanged.
E.g. Cylinder filled with gas & piston
Open System
Both energy and mass can be exchanged.
E.g. Gas turbine, I.C. Engine

## Slide 6: THERMODYNAMIC PROPERTIES
Thermodynamic Properties – It is measurable & Observable characteristics of the system.
Extensive: Depend on mass/size of system (Volume [V]), Energy
Intensive: Independent of system mass/size (Pressure [P], Temperature [T])
Specific: Extensive/mass (Specific Volume [v])

## Slide 7: What is Force?
In physics, a force is any interaction that, when unopposed, will change the motion of an object. A force can cause an object with mass to change its velocity (which includes to begin moving from a state of rest), i.e., to accelerate. Force can also be described intuitively as a push or a pull. A force has both magnitude and direction, making it a vector quantity. It is measured in the SI unit of newtons and represented by the symbol F. We know that, F = ma.

## Slide 8: PRESSURE
P = Force/Area
Pa, Kpa,Bar, N/m2
Types:
  Absolute
  Gage (Vacuum)
  Atmospheric
Pabs =Patm +/- Pgauge
PRESSURE
PRESSURE

## Slide 9: Volume
Three dimensional space occupied by an object
Unit- M3 , Liter
Volume
Volume

## Slide 10: What is Energy?
During Newton’s time there was no concept of “energy”. Sir Isaac Newton just gave the world concept of “force”.
In physics, energy (unit “Joule”) is the quantitative property that must be transferred to an object in order to perform work on, or to heat the object.
K.E. = (1/2)mv^2. Concept of velocity square was new at that time.

## Slide 11: Internal energy
Internal energy (also called thermal energy) is the energy an object or substance is due to the kinetic and potential energies associated with the random motions of all the particles that make it up.
Monatomic ideal gas: Eint = (3/2)nRT
Diatomic ideal gas: Eint = (5/2)nRT
Polyatomic ideal gas: Eint = (6/2)nRT
Internal Energy
Internal Energy [U]

## Slide 14: What is Heat?
During Newtonian era heat was considered as to be a substance, if it is available in any matter then it will be warmer. It was called “calor” from which the word calorie came. (Example: if we have more salt in a substance it becomes salty, more sugar makes it sweet and more chili makes it spicy, similarly more calor makes thing warm.
In 1845 James Prescott Joule discovered the link between mechanical work and the generation of heat. Later these developments led to the theory of conservation of energy, formalized largely by William Thomson (A.K.A. Lord Kelvin) as the field of thermodynamics.
Q = (mc)dT + (mL). Here, c = specific heat & L = latent heat.

## Slide 15: What is Work?
It is also possible to change the temperature of a substance by doing work. Work can do transfer energy into or out of a system. This realization helped establish the fact that is heat is a form of energy. Mr. James Prescott Joule (1818–1889) performed many - many experiments to establish the, ”mechanical equivalent of heat” — the work needed to produce the same effects as heat transfer.
Concept of Force: F = d(mv)/dt
Concept of Energy: E = ∫ FdS
Do the integration to find velocity squared.

## Slide 16: What is Power?
In physics, power is the amount of energy converted or, work done per unit time. In SI, the unit of power is the watt, equal to one joule per second. Power is a scalar quantity. Dimension [L^2][M][T^-3].
P = E/t = W/t = FS/t = F(v)
For Electrical and Electronics Engineers:
P = W/t = (QV)/t = V.(Q/t) = V.I = (RI).I = RI2, [P.S. V = volt, not volume]
But we also denote pressure with P, as P = F/A = FS/AS = W/V
So, to avoid confusion from the next slides throughout the course we will denote power by Pw and Pressure by Pr.

## Slide 17: What is Temperature?
Temperature is a physical property of matter that quantitatively expresses hot and cold.
Absolute zero temperature: – 273°C = – 460°F = Zero Kelvin
Kinetic interpretation of Temperature:
Formulas:
Where, kB is the Boltzmann constant and equal to 1.38065 × 10−23 J/K.
Also: . Here, S = Entropy and, W = Work Done.
As temperature flows from high temp. to low temp. So, dS≥0.

## Slide 18: Temperature
Q
m c Δt

## Slide 19: What is Entropy?
What is happiness? How can we measure happiness? If you donate a $100 note to a beggar and, a $100 note to a billionaire then who will become happier? Why? Can we measure change in happiness?
The change in happiness between poor beggar and wealthy billionaire can be measured by difference in existing amount of money (+ or -) & divided by existing amount of money. Similarly:
Formula: dS = dQ/T , [where, dS is change in entropy ≥ 0].

## Slide 20: What is Entropy?
Entropy is defined as the non-work producing form of energy. So, it is also regarded as the energy that is not available for performing useful work within a certain environment.
Entropy is a measure of irreversibility or disorder or randomness of a system. An ordered system has low entropy. A disordered system has high entropy.

## Slide 21: Entropy as Disorder (Milk and Coffee):

## Slide 22: Entropy as Chaos:

## Slide 23: Entropy as irreversibility:

## Slide 24: Entropy as Information:

## Slide 25: Entropy as Arrow of Time:
Here beside you can see an animation of a simple pendulum which follows the following equation:
Can you tell me whether the animation is playing forward or backward?
How can you tell?

## Slide 26: Which way the train is moving?

## Slide 28: What is Enthalpy?

## Slide 29: What is Enthalpy?
Enthalpy of a system indicates the energy which is defined as the sum of internal energy of a system and the product of the pressure and volume:
h = U + PV = U + nRT = U + nkBNAT = U + (1/3)mn.
S.T.P. : 0 oC (273.15 K, 32 oF) and 750mm Hg (1 bar)
N.T.P. : 20oC (293.15 K, 68oF) and 760 mm Hg(1 atm)
Molar volume of ideal gas at S.T.P. = 22.4 Lt.

## Slide 30: What is Enthalpy?

## Slide 31: What is Enthalpy?

## Slide 32: What is Enthalpy?

## Slide 33: Thermodynamic Systems:
Isobaric: P constant
Isochoric: V constant
Isothermal: T constant
Isentropic: S constant
Isenthalpic: h constant
Adiabatic System: ???
Cp - Cv = R and γ = Cp/Cv
Monatomic ideal gas: γ = 1.6666666
Diatomic ideal gas: γ = 1.4
Polyatomic ideal gas: γ = 1.3333333

## Slide 34: Laws of Thermodynamics:
BME lecture final ter
m week:1

## Slide 35: Zeroth Law of Thermodynamics

## Slide 36: First Law of Thermodynamics

## Slide 37: Second Law of Thermodynamics

## Slide 38: Explain why this happens:
Remember the train animation shown earlier? Is it possible to happen that a tennis ball is resting at ground and suddenly it start to shake and bounce on its own up and down? Or are you playing the video reverse?

## Slide 39: Micro-State vs. Macro-State

## Slide 40: Probability

## Slide 42: All Energy Transmission is Inefficient:

## Slide 43: Third Law of Thermodynamics

## Slide 44: Third Law of Thermodynamics

## Slide 46
Question: Calculate the change in entropy to convert 1kg of 0oC ice into 100oC steam at 1 atm pressure.
https://rashidedu.files.wordpress.com/2016/05/1-thermodynamics.pdf
Solution:
Change in entropy to convert 0oC ice into 0oC water:
Change in entropy to convert 0oC water into 100oC water:
Change in entropy to convert 100oC water into 100oC steam:
Total change in entropy = 8.6 kJ/kg

## Slide 47
Entropy and the Clausius Inequality
The second law of thermodynamics leads to the definition of a new property called entropy, a quantitative measure of microscopic disorder for a system. Entropy is a measure of energy that is no longer available to perform useful work within the current environment. To obtain the working definition of entropy and, thus, the second law, let's derive the Clausius inequality.
Consider a heat reservoir giving up heat to a reversible heat engine, which in turn gives up heat to a piston-cylinder device as shown below.

## Slide 48
We apply the first law on an incremental basis to the combined system composed of the heat engine and the system.
Ein  Eout  Ec
QR  (Wrev  Wsys )  dEc
where Ec is the energy of the combined system. Let Wc be the work done by the combined system. Then the first law becomes
Wc  Wrev  Wsys
QR  Wc  dEc
If we assume that the engine is totally reversible, then
QR  Q TR T
Q
T
R R
 T Q
The total net work done by the combined system becomes
T
c R
c
W  T Q  dE

## Slide 49: Now the total work done is found by taking the cyclic integral of the incremental work.
If the system, as well as the heat engine, is required to undergo a cycle, then
and the total net work becomes
If Wc is positive, we have a cyclic device exchanging energy with a single heat reservoir and producing an equivalent amount of work; thus, the Kelvin-Planck statement of the second law is violated. But Wc can be zero (no work done) or negative (work is done on the combined system) and not violate the Kelvin-Planck statement of the second law. Therefore, since TR > 0 (absolute temperature), we conclude

## Slide 50: Let’s look at a simple irreversible cycle on a p-v diagram with two processes
P

.
1
. 2
A
B
Let A be irreversible and B be reversible

## Slide 51: By Clausius Inequality  T )AB  0
Irreversible cycle
Q
Evaluate cyclic integral
 0
1
B
2 Q 
  T 
1
A
cycle
Q  2 Q 
  T 
 T 
(non-rev)
(rev)

## Slide 52: Irreversible cycle
For the reversible process, B, dS=Q/dT, thus:
1 1
A
cycle
Q  2 Q 
2
  T    dS  0
 T 
Rearranging and integrating dS:
A
2 Q 
S   T 
1

## Slide 53: Second Law of Thermodynamics
This can be viewed as a mathematical statement of the second law (for a closed system).
Entropy is a non-conserved property!
A
2 Q 
S  S2  S1   T 
1

## Slide 54: 2 Q 
We can write entropy change as an equality by adding a new term:
Sgen
1
A
S2  S1 
entropy change
 T 

entropy transfer due to heat transfer
entropy production or generation

## Slide 55: Entropy generation
Sgen  0 is an actual irreversible process.
Sgen = 0 is a reversible process.
Sgen  0 is an impossible process.

## Slide 56: Entropy transfer and production
What if heat were transferred from the system?
The entropy can actually decrease if
 Sgen
1
A
2 Q 
 T 
and heat is being transferred away
from the system so that Q is negative.

## Slide 57: Entropy Production
Sgen
quantifies irreversibilities. The
larger the irreversibilities, the greater the value of the entropy production, Sgen
.
A reversible process will have no entropy production.

## Slide 58: Entropy transfer and production
S2 – S1
because Sgen is always positive.
< 0, if Q is negative and
= 0 if Q = 0 and Sgen = 0.
= 0 if Q is negative and
 Sgen
1
A
2 Q 
 T 
 Sgen
1
A
2 Q 
> 0, Q could be + or –; if –,  T 
 Sgen
1
A
2 Q 
 T 

## Slide 59: Isentropic processes
Note that a reversible (Sgen = 0), adiabatic (Q = 0) process is always isentropic (S1 = S2)
But, if the process is merely isentropic with S1 = S2, it may not be a reversible adiabatic process.
For example, if Q  0 and
 Sgen
1
A
2 Q 
 T 

## Slide 60
Entropy generation
Consider
S2  S1 
What if we draw our system boundaries so large that we encompass all heat transfer interactions? We would thereby isolate the system.
Sgen
1
A
2 Q 
 T 


## Slide 61
16
Entropy changes of isolated systems
And then
Sgen
1

A
2 Q 
S2  S1 
 T 
0
 Sgen
S2  S1
But Sgen0. So, the entropy of an isolated system always increases. (This is the source of the statement, ‘The world is running down.’)

## Slide 62
Entropy
It is tabulated just like u, v, and h.
x(sg  sf )
Also, s  sf
And, for compressed or subcooled liquids,
s(T, p)  sf (T)

## Slide 63
The entropy of a pure substance is determined from the tables, just as for any other property

## Slide 64: Ts Diagram for Water

## Slide 65: Ts diagrams
Recall that the P-v diagram was very important in first law analysis, and that
w   pdV
Work was the area under the curve.

## Slide 66: For a Ts diagram
21
int rev
 T 

dS   Q 
 TdS
2
  TdS
δQint rev
Qint rev
1
If the internally reversible process also is isothermal at some temperature To:
2
Rearrange:
Integrate:
 To  dS  To S
1
Qint rev

## Slide 67
On a T-S diagram, the area under the process curve represents the heat transfer for internally reversible processes
d

## Slide 68: Entropy change of a thermal reservoir
T
For a thermal reservoir, heat transfer occurs at constant temperature…the reservoir doesn’t change temperature as heat is removed or added:
S   Q
T
Since T=constant:
S  Q

## Slide 69: Derivation of Tds equations:
dQ – dW = dU
For a simple closed
system:
The work is given by:
dW = PdV
Substituting gives:
dQ = dU + PdV

## Slide 70
More derivation….
For a reversible process:
TdS = dQ
Make the substitution for Q in the energy equation:
TdS = dU + PdV
Or on a per unit mass basis:
Tds = du + Pdv

## Slide 71: Tds Equations
Entropy is a property. The Tds expression that we just derived expresses entropy in terms of other properties. The properties are independent of path….We can use the Tds equation we just derived to calculate the entropy change between any two states:
Tds = du +Pdv
Starting with enthalpy, it is possible to develop a second Tds equation:
Tds = dh - vdP

## Slide 72: Let’s look at the entropy change for an incompressible substance:
dT
T
c(T)
ds 
We start with the first Tds equation:
Tds = cv(T)dT + Pdv
For incompressible substances, v  const, so dv = 0.
We also know that cv(T) = c(T), so we can write:

## Slide 73: Entropy change of an incompressible substance
T2 c(T)
s2  s1   T dT
T1
1
2
s2  s1  c ln
T
T
Integrating
If the specific heat does not vary with temperature:

## Slide 74: Entropy change for an ideal gas
dh  cpdT And
p
p
Tds  c dT  RT dp
Start with 2nd Tds equation
Tds = dh - vdp
Remember dh and v for an ideal gas?
v=RT/p
Substituting:

## Slide 75: Change in entropy for an ideal gas
dT  R dp T p
ds  c
p
Dividing through by T,
Don’t forget, cp=cp(T)…..a function of temperature! Integrating yields
dT p
R ln 2
p1
T
1
T2
s2  s1   cp (T)
T

## Slide 76: Entropy change of an ideal gas for constant specific heats: approximation
Now, if the temperature range is so limited that cp  constant (and cv 
constant),
1
2
p
p
T T
dT T
 c ln
c

1
1
2
s2  s1  cp ln
p
R ln p2
T
T

## Slide 77: Entropy change of an ideal gas for constant specific heats: approximation
Similarly it can be shown from
Tds = du + pdv
that
1
1
2
s2  s1  cv ln
v
R ln v 2
T
T

## Slide 78
T
dT p
R ln 2
p1
s2  s1   cp (T)
Entropy change of an ideal gas for variable specific heats: exact analysis
Integrating..
T2
T
1
T
dT
 cp T1
To evaluate entropy change, we’ll have to evaluate the integral:
T2

## Slide 79
T1
 cp
T2
T0 T0
T
dT
T
dT
dT
T2
 cp T   cp
T1
2 1
 so (T )  so (T )
And so(T), the reference entropy, is tabulated in the ideal gas tables for a reference temperature of T = 0 and p = 1
atm.
Entropy change of an ideal gas for variable specific heats: exact analysis
Evaluation of the integral

## Slide 80: Entropy change of an ideal gas for variable specific heats: exact analysis
Only  cpdT is tabulated. The  cvdT
is not.
1
2
1
o
2
o
1
2
So, s
p
p
s (T )  R ln
 s  s (T ) 

## Slide 81: Entropy change of an ideal gas
Note that the entropy change of an ideal gas, unlike h and u, is a function of two variables.
Only the reference entropy, so, is a function of T alone.

## Slide 83: Conclusion: