## Slide 1: Thermodynamics Lecture 02
Basic Mechanical Engineering

## Slide 2: A Quick Review:
BME lecture final ter
m week:1

## Slide 3: THERMODYNAMICES
THERMO--- Heat Released
DYNAMICS ----- Mechanical Action For doing work
The study of the effects of work, heat flow, and energy on a system
Movement of thermal energy
Engineers use thermodynamics in systems ranging from nuclear power plants to electrical components.
Thermodynamics is the study of the effects of work, heat, and energy on a system
Thermodynamics is only concerned with macroscopic (large- scale) changes and observations

## Slide 4
BOUNDARY- | System | & Surrounding | are
separated by | some | Imaginary Or | real
SYSTEM, SURROUNDING ,UNIVERSE
SYSTEM-Area under thermodynamic study
SURROUNDING – Area outside the system
Surface/Layer/Partition
UNIVERSE – System & together is called Universe
Surroundings put

## Slide 5: ISOLATED, CLOSED AND OPEN SYSTEMS
4
Isolated System
Neither energy nor mass can be exchanged.
E.g. Thermo flask
Closed System
Energy, but not mass can be exchanged.
E.g. Cylinder filled with gas & piston
Open System
Both energy and mass can be exchanged.
E.g. Gas turbine, I.C. Engine

## Slide 6: THERMODYNAMIC PROPERTIES
Thermodynamic Properties – It is measurable & Observable characteristics of the system.
Extensive: Depend on mass/size of system (Volume [V]), Energy
Intensive: Independent of system mass/size (Pressure [P], Temperature [T])
Specific: Extensive/mass (Specific Volume [v])

## Slide 7: PRESSURE
P = Force/Area
Pa, Kpa,Bar, N/m2
Types:
  Absolute
  Gage (Vacuum)
  Atmospheric
Pabs =Patm +/- Pgauge
PRESSURE
PRESSURE

## Slide 8: Volume
Three dimensional space occupied by an object
Unit- M3 , Liter 1 m3 = 103 lit
Volume
Volume

## Slide 9: Temperature
Quantitative indication of Degree of Hotness & coldness of the body.
Unit- 0C , K , F
Thermometer
Thermometry
Temperature
Temperature Scale

## Slide 10: Internal energy
Internal energy (also called thermal energy) is the energy an object or substance is due to the kinetic and potential energies associated with the random motions of all the particles that make it up.
Internal energy is defined as the energy associated with the random, disordered motion of molecules.
Unit- KJ , Joule
Internal Energy
Internal Energy [U]

## Slide 11: Enthalpy
Total Heat content of Body
Heat supplied to the body Enthalpy increases & decreases when heat is removed
Enthalpy is a measure of the total energy of a thermodynamic system.
Enthalpy
Enthalpy

## Slide 12: Work
Work = Force x Displacement (Nm) ( Joule)
Energy in Transient
Path function
High grade energy
Work done by the system on the surrounding
-Positive work
Work done on the system by surrounding – Negative work

## Slide 13: HEAT
Energy transfer by virtue of temperature difference
Transient form of energy
Path function
Low grade energy
Negative heat- heat transferred from the system ( heat rejection)
Positive heat – heat transferred from surrounding to system (heat absorption)

## Slide 14: HEAT
Energy transfer by virtue of temperature difference
Transient form of energy
Path function
Low grade energy
Negative heat- heat transferred from the system ( heat rejection)
Positive heat – heat transferred from surrounding to system (heat absorption)
HEAT
CONCEPT
hot
cold
heat
26 °C
26 °C

## Slide 15: Work & Heat
Work is the energy transferred between a system and environment when a net force acts on the system over a distance.
The sign of the work
Work is positive when the force is in the direction of motion
Work is negative when the force is opposite to the motion
WORK
WORK

## Slide 16: LAWS OF THERMODYNAMICS
FIRST LAW OF THERMODYNAMICS (LAW OF ENERGY CONSERVATION)
SECOND LAW OF THERMODYNAMICS
ZEROTH LAW OF THERMODYNAMICS

## Slide 18: Heat Engine, Heat Pump & Refrigerator:

## Slide 19: Comparison:

## Slide 20: Rudolf Clausius
Name: Rudolf Julius Emanuel Clausius (2 January 1822 – 24 August 1888) was a German physicist and mathematician and is considered one of the central founders of science of thermodynamics. By his restatement of Sadi Carnot's principle known as the Carnot cycle, he gave the theory of heat a truer and sounder basis. His most important paper, "On the Moving Force of Heat", published in 1850, first stated the basic ideas of the 2nd law of thermodynamics. In 1865 he introduced the concept of entropy. In 1870 he introduced the virial theorem which applied to heat.

## Slide 21: William Thomson, 1st Baron Kelvin
Sir William Thomson, 1st Baron Kelvin, (26 June 1824 – 17 December 1907) was an Irish-Scottish (of Ulster Scots heritage) mathematical physicist and engineer who was born in Belfast in 1824. At the University of Glasgow he did important work in mathematical analysis of electricity and formulation of 1st & 2nd laws of thermodynamics and did much to unify the emerging discipline of physics in its modern form.

## Slide 22: Max Planck
Max Karl Ernst Ludwig Planck (23 April 1858 – 4 October 1947) was a German theoretical physicist whose discovery of energy quanta won him the Nobel Prize in Physics in 1918.
Mostly famous for discovering Albert Einstein and formulating: E = h (f), h = Planck’s constant.

## Slide 25: Comparison:

## Slide 26: Kelvin Planck Statement:
The Kelvin–Planck statement (or the Heat Engine Statement) of the second law of thermodynamics states that it is impossible to devise a cyclically operating heat engine, the effect of which is to absorb energy in the form of heat from a single thermal reservoir and to deliver an equivalent amount of work. This implies that it is impossible to build a heat engine that has 100% thermal efficiency.

## Slide 29: Clausius Statement:
It is impossible for heat to move by itself from a lower temperature reservoir to a higher temperature reservoir. That is, heat transfer can only occur spontaneously in the direction of temperature decrease. For example, we cannot construct a refrigerator that operates without any work input.

## Slide 31
Whenever we want to convert work to heat even the efficiency losses like friction will also dissipates as Heat. So, there must be no losses because even losses are converting to heat energy.
But this will not happen while converting heat to work. Because the losses are also dissipated as Heat. Means some of heat energy is lost during this process. So, we can't convert heat completely in to work.
Lost means it can’t be converted into a form to perform useful work.
Hence, the entropy of the universe in every moment is increasing.
While there is no limit to the ability to convert work to heat, there is a limit on converting heat to work, as the minimum temperature can be only low as – 273°C but not lower than that.
Why work can be completely converted into heat but not vice versa?

## Slide 32: C.O.P.

## Slide 33: Equivalence of Kelvin Plank and Clausius Statement

## Slide 34: Perpetual Motion Machine of First Kind

## Slide 35: Perpetual Motion Machine of Second Kind
Why doesn't this work?
Can anyone explain???

## Slide 36: Perpetual Motion Machine of Third Kind

## Slide 37: Pop Quiz: What kind of PMM is this one?

## Slide 39
Ludwig Eduard Boltzmann (German; February 20, 1844 – September 5, 1906) was an Austrian physicist and philosopher. His greatest achievement was in the development of statistical mechanics, which explains and predicts how the properties of atoms (such as mass, charge, and structure) determine the physical properties of matter (such as viscosity, thermal conductivity, and diffusion). Boltzmann coined the word ergodic while he was working on a problem in statistical mechanics.
TASK:
What is Boltzmann Brain?
What is Boltzmann Demon?
What is Boltzmann Constant?

## Slide 40: Q = mcΔt
Q – Energy (Heat gained or lost)
m – Mass
c – Specific Heat
Δt – Change in Temperature
Q
m c Δt

## Slide 41: HEAT RESERVOIR, HEAT SOURCE, HEAT SINK
HEAT RESERVOIR- Source of infinite heat energy & finite amount of heat addition & heat rejection from it will not change its temperature
E. g. Ocean, River, Large bodies of water Lake
HEAT SOURCE- Heat reservoirs which supplies heat to system is called heat source
HEAT SINK- Heat reservoir which receives absorbs heat from the system

## Slide 42: 2ND LAW OF THERMODYNAMICS KELVIN –PLANCK’S STATEMENT
It is impossible to construct a machine which operates in cycle whose sole effect is to
heat into amount of
convert equivalent work

## Slide 43
2ND LAW OF THERMODYNAMICS CLAUSIUS STATEMENT
It is impossible to construct a machine which operates in cycle whose sole effect is to transfer heat from LTB to HTB without consuming external work
CONCEPT
STATEMENT

## Slide 44: 2nd Law: Clausius and Kelvin Statements
22
Clausius statement (1850)
Heat cannot by itself pass from a colder to a hotter body; i.e. it is impossible to
build a “perfect” refrigerator.
The hot bath gains entropy, the cold bath loses it.
ΔSuniv= Q2/T2 – Q1/T1 = Q/T2 – Q/T1 <
0.
Kelvin statement (1851)
No process can completely convert heat into work; i.e. it is impossible to build a “perfect” heat engine.
ΔSuniv= – Q/T < 0.
1st Law: one cannot get something for nothing (energy conservation).
2nd Law: one cannot even break-even (efficiency must be less
Q1 = Q2 = Q
M is not active.

## Slide 45: HEAT ENGINE
Thermodynamic system/Device which operate in cycle converts the heat into useful work.
HEAT ENGINE
HEAT ENGINE

## Slide 46: HEAT ENGINE
Efficiency = e = W/Qs
Qhot
Qhot Qcold
W
e
1 Qcold
Note: The temperatures must be measuredin Kelvins!!!
hot
Carnot
T
Qhot Qhot
1 Tcold
e

## Slide 47: HEAT PUMP
Thermodynamic system/Device which operate in cycle converts the heat into useful work.
Cold Reservoir, TC
Hot Reservoir, TH
QH
WORK
P
QC

## Slide 48: HEAT PUMP & REFRIGERATOR
HEAT PUMP
Cold Reservoir, TC
R
Hot Reservoir, TH
QH
QC
W
Cold Reservoir, TC
P
Hot Reservoir, TH
QH
QC
W

## Slide 49: Reversible Engine: the Carnot Cycle
27
Stage 1 Isothermal expansion at temperature T2, while the entropy rises from S1 to S2.
The heat entering the system is
Q2 = T2(S2 – S1).
Stage 2 adiabatic (isentropic) expansion at entropy S2, while the temperature drops from T2 to T1.
Stage 3 Isothermal compression at temperature T1, while the entropy drops from S2 to S1.
The heat leaving the system is
Q1 = T1(S2 – S1).
Stage 4 adiabatic (isentropic) compression at entropy S1, while the temperature rises from T1 to T2.
Since Q1/Q2 = T1/T2,
η = ηr = 1 – T1/T2.

## Slide 50: Gibbs Free Energy
In thermodynamics, the Gibbs free energy is a thermodynamic potential that can be used to calculate the maximum of reversible work that may be performed by a thermodynamic system at a constant temperature and pressure. The Gibbs free energy is the maximum amount of non-expansion work that can be extracted from a thermodynamically closed system (can exchange heat and work with its surroundings, but not matter) in the standard state. This maximum can be attained only in a completely reversible process. When a system transforms reversibly from an initial state to a final state, the decrease in Gibbs free energy equals the work done by the system to its surroundings, minus the work of the pressure forces.

## Slide 51: Gibbs Free Energy
The Gibbs free energy initially called available energy was developed in the 1870s by the American scientist Josiah Willard Gibbs.
The Gibbs Free Energy is also the thermodynamic potential minimized when a system reaches chemical equilibrium at constant pressure and temperature. Its derivative with respect to the reaction coordinate of the system vanishes at the equilibrium point. As a reduction in is necessary for a reaction to be spontaneous at constant pressure and temperature.
The initial state of the body, according to Gibbs, is supposed to be such that "the body can be made to pass from it to states of dissipated energy by reversible processes". In his 1876 magnum opus On the Equilibrium of Heterogeneous Substances, a graphical analysis of multi-phase chemical systems, he engaged his thoughts on chemical free energy in full.

## Slide 60: Gibbs Free Energy

## Slide 61: Recall: Suniv and Spontaneous Processes
The total entropy change of the universe (Suniv) for any spontaneous process is positive.
+ Suniv
Suniv = Ssys + Ssurr

## Slide 62: Suniv and Gibbs Free Energy (G)
Calculating Suniv is not convenient.
Suniv = Ssys + Ssurr
Gibbs proposed a new thermodynamic state function that is derived from three other state functions for the system.
Enthalpy, Entropy, and Temperature.

## Slide 63: Gibbs Free Energy (G)
G = H  TS
The Gibbs Free Energy change for a given process is
G = H  TS (at constant T and P)

## Slide 64
Suniv and Gibbs Free Energy (G)
Entropy S is maximized at equilibrium
Free energy G is minimized at equilibrium.

## Slide 65: Gibbs Free Energy G
Without derivation:
TSuniv = Hsys  T Ssys
TSuniv = G
G
When G for a given process is negative, the process is spontaneous in the forward direction (as written).

## Slide 66: Predicting Spontaneity and G
Negative G means the process is spontaneous (as written; in the forward direction).
Positive G means the process is nonspontaneous (as written). However, it is spontaneous in the reverse direction!
If G = 0, the reaction is at equilibrium.

## Slide 67: Gibbs Free Energy (G) and Predicting Spontaneous Processes
The sign of the Gibbs Free Energy for a given process will depend on the signs of
H and S.
G = H  T S
We can predict whether a given process will b spontaneous by analyzing the signs of H and S.

## Slide 68: H, S, and the Sign of G
Sign of H | Sign of S | Sign of G | Type of Process
negative | positive | negative | spontaneous at all temperatures
positive | negative | positive | nonspontaneous at all temperatures
positive | positive | () or (+) | Spontaneous if the temperature is high enough
negative | negative | (+) or () | Spontaneous if the temperature is low enough
G = H  T S

## Slide 69: Case 1: H and S Agree (Spontaneous)
G = ()  (+)(+)
G = a negative number (any T)
T in K, so always a positive number!
When H is negative and S is positive, G is always negative. The reaction is spontaneous in the forward direction (any T).
G = H  T S
Negative term
G = ()  T (+)

## Slide 70: Case 2: H and S Agree (Nonspontaneous)
H is positive and S is negative, so G is always positive. The reaction is nonspontaneous in the forward direction (any T). Spontaneous in reverse direction.
G = H  T S
G = (+)  T ()
G = (+)  (+)()
G = a positive number (any T)
T in K, so always a positive number!
Positive term

## Slide 71: Case 3: H and S Disagree (G “Decides”)
H is positive and S is positive, so G is negative or positive depending on the temperature. The reaction is spontaneous in the forward direction if T is high enough.
G = H  T S
G = (+)  T (+)
G = (+)  (+)(+)
T in K, so always a positive number!
Positive term

## Slide 72: Case 3: H and S Disagree (G “Decides”)
The reaction is spontaneous in the forward direction if T is high enough.
G = H  T S
G = (+)  T (+)
G = (+)  (+)(+)
G = a positive number (at low T)
G = a negative number (at high T)
Subtract a large positive term
If T is high, subtract a larger number than H

## Slide 73: Case 4: H and S Disagree (G “Decides”)
H is negative and S is negative, so G is negative or positive depending on the temperature. The reaction is spontaneous in the forward direction if T is low enough.
G = H  T S
G = ()  T ()
G = ()  (+)()
T in K, so always a positive number!
negative term

## Slide 74: Case 4: H and S Disagree (G “Decides”)
G = ()  T ()
G = ()  (+)()
G = a negative number (at low T)
G = a positive number (at high T)
The reaction is spontaneous in the forward direction if T is low enough.
G = H  T S
a positive term
overall
If T is low, add a smaller number than H

## Slide 75: Summary: Gibbs Free Energy (G)
G = H  T S
When H is () and S is (+) , G is always (). Spontaneous in the forward direction (any T).
H is (+) and S is (), so G is always (+). Nonspontaneous in the forward direction (any T).

## Slide 76
Summary: Gibbs Free Energy (G)
G = H  T S
H is (+) and S is (+), so G is () or (+) depending on the temperature.
Spontaneous in the forward direction if T is high enough.

## Slide 77
Summary: Gibbs Free Energy (G)
G = H  T S
H is () and S is (), so G is (+) or () depending on the temperature.
Spontaneous in the forward direction if T is low enough.

## Slide 78: End of Lecture 2